From lang@strat04.met.fu-berlin.de Mon Feb 22 17:25 MET 1999
Date: Mon, 22 Feb 1999 17:21:22 +0100 (MET)
From: Ulrike Langematz <lang@strat01.met.fu-berlin.de>
To: morcrette@ecmwf.int, beagley@nimbus.yorku.ca,
        tgs@chinook.physics.utoronto.ca, nmcfarlane@ec.gc.ca,
        koshyk@mam.physics.utoronto.ca, wal@met.reading.ac.uk,
        swsthubn@met.rdg.ac.uk, pascal.simon@meteo.fr,
        marielle.amodei@meteo.fr, wan@atm.ox.ac.uk,
        pawson@polska.gsfc.nasa.gov, kph@gfdl.gov, rjw@gfdl.gov,
        cddhr@giss.nasa.gov, cdnkb@giss.nasa.gov, coy@demeter.gsfc.nasa.gov,
        t.d.fairlie@larc.nasa.gov, w.l.grose@larc.nasa.gov,
        pierce@kelvin.larc.nasa.gov, manzini@dkrz.de, kshibata@mri-jma.go.jp,
        kitoh@mri-jma.go.jp, kodera@mri-jma.go.jp, boville@ncar.ucar.edu,
        farrara@atmos.ucla.edu, mechoso@atmos.ucla.edu,
        rswinbank@dao.gsfc.nasa.gov, G.Roff@BoM.gov.au, frode@zardoz.nilu.no,
        w.zhong@ic.ac.uk, lang@strat01.met.fu-berlin.de
Subject: GRIPS-Radiation-Intercomparison

Dear everyone,

after my email from last November I got some comments and 
suggestions which I would like to forward to you. 


If possible, several radiative heating rate profiles (latitude-
height cross sections) should be computed:

   a) using the standard input dataset, 
      - but gaseous absorption by O3, CO2 and H2O only  (to allow 
        for a comparison with those radiative codes who don't 
        include any other tracegases)
      - use an isothermal temperature profile with T = 280 K

   b) using the standard input dataset, 
      - but gaseous absorption by O3, CO2 and H2O only
      - use the CIRA-temperature climatology

    c) using the full standard input dataset

Additionally profiles from your already existing control runs for
mean January conditions are welcome as well, to get a feeling of the
discrepancies arising from using different radiation models without 
any constraints on the input data.


Furthermore, I have extended the standard input dataset by some fields,
which might be necessary for some of the radiative transfer codes.

These are:

    1) A latitude-height distribution for January of
       -  methane (ch4)

    2) Latitude distributions for January of
       -  sea level pressure (unit: Pa)  (slp)
       -  surface pressure   (unit: Pa)  (sfc)
       -  2m temperature     (unit: K)   (t2m)

    3) The constants-file has been completed by all trace gases
       listed in the IPCC-94 report.

    4) The shortwave clear-sky albedo has been replaced by a
       zonal-mean field to enable a direct comparison of 
       results from 2d offline radiation codes.

You will find the files with extensions .gra for GrADS-datafile,
.ctl for GrADS-control file and .ps for postscript-file in the 
same directory as the other data:

	/home/guest/GRIPS/radcomp/inputdata   .


I hope, it will be possible for all of you to do the computations
successfully.


There will be two opportunities in the near future to present and 
discuss results from this radiative code intercomparison: The 
GRIPS Workshop in Reading at the end of March and the IUGG meeting 
in Birmingham in July.
If you could provide me with your data early enough, I would try 
hard to include them into the presentations. The more results we
will have for the GRIPS workshop, the more we can discuss them and 
decide the next steps.


With my best regards,
Ulrike


<<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>>
Dr. Ulrike Langematz

Institut fuer Meteorologie              Tel: 49 - 30 - 838 711 65
Freie Universitaet Berlin               Fax: 49 - 30 - 838 711 28
Carl-Heinrich-Becker-Weg 6-10           email: lang@strat01.met.fu-berlin.de
12165 Berlin 
Germany
<<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>><<>>